Pressure drop in gas pipelines
### Gas line sizing
The pressure drop in gas lines is typically low in gas-producing facilities because the piping segment lengths are short. The pressure drop has a more significant impact upon longer segments such as gas-gathering pipelines, transmission pipelines, or relief or vent piping.
The velocity in gas lines should be less than 60 to 80 ft/sec to minimize noise and allow for corrosion inhibition. A lower velocity of 50 ft/sec should be used in the presence of known corrosives such as CO2. The minimum gas velocity should be between 10 and 15 ft/sec, which minimizes liquid fallout.
Gas velocity is expressed in Eq. 6 as
 (Eq. 6)
where
Vg	=	gas velocity, ft/sec,
Qg	=	gas-flow rate, MMscf/D,
T	=	gas flowing temperature, °R,
P	=	flowing pressure, psia,
Z	=	compressibility factor, dimensionless,
and
d	=	pipe ID in.

Source: http://petrowiki.org/Pipeline_design_consideration_and_standards#Gas_line_sizing
### Liquid line sizing
The liquid velocity can be expressed as
 (Eq. 5)
where
QL	=	fluid-flow rate, B/D
and
d	=	pipe ID, in.

In piping systems where solids might be present or where water could settle out and create corrosion zones in low spots, a minimum velocity of 3 ft/sec is normally used. A maximum velocity of 15 ft/sec is often used to minimize the possibility of erosion by solids and water hammer caused by quickly closing a valve.
### Gas line sizing
The pressure drop in gas lines is typically low in gas-producing facilities because the piping segment lengths are short. The pressure drop has a more significant impact upon longer segments such as gas-gathering pipelines, transmission pipelines, or relief or vent piping.
The velocity in gas lines should be less than 60 to 80 ft/sec to minimize noise and allow for corrosion inhibition. A lower velocity of 50 ft/sec should be used in the presence of known corrosives such as CO2. The minimum gas velocity should be between 10 and 15 ft/sec, which minimizes liquid fallout.
http://petrowiki.org/Pipeline_design_consideration_and_standards#Liquid_line_sizing

## Pressure drop for gas flow
### General equation
The general equation for calculating gas flow is stated as
 (Eq. 11)
where
w	=	rate of flow, lbm/sec,
g	=	acceleration of gravity, 32.2 ft/sec2,
A	=	cross-sectional area of pipe, ft2,
V1‘	=	specific volume of gas at upstream conditions, ft3/lbm,
f	=	friction factor, dimensionless,
L	=	length, ft,
D	=	diameter of the pipe, ft,
P1	=	upstream pressure, psia,
and
P2	=	downstream pressure, psia.

Assumptions: no work performed, steady-state flow, and f = constant as a function of the length.
### Simplified equation
For practical pipeline purposes, Eq. 11 can be simplified to
 (Eq. 12)
where
P1	=	upstream pressure, psia,
P2	=	downstream pressure, psia,
S	=	specific gravity of gas,
Qg	=	gas flow rate, MMscf/D,
Z	=	compressibility factor for gas, dimensionless,
T	=	flowing temperature, °R,
f	=	Moody friction factor, dimensionless,
d	=	pipe ID, in.,
and
L	=	length, ft.

The compressibility factor, Z, for natural gas can be found in Fig. 7.
Fig. 7—Compressibility of low-molecular-weight natural gases (courtesy of Natl. Gas Processors Suppliers Assn.).

Three simplified derivative equations can be used to calculate gas flow in pipelines:
- The Weymouth equation
- The Panhandle equation
- The Spitzglass equation
All three are effective, but the accuracy and applicability of each equation falls within certain ranges of flow and pipe diameter. The equations are stated next.
#### Weymouth equation
This equation is used for high-Reynolds-number flows where the Moody friction factor is merely a function of relative roughness.
 (Eq. 13)
where
Qg	=	gas-flow rate, MMscf/D,
d	=	pipe inside diameter, in.,
P1	=	upstream pressure, psia,
P2	=	downstream pressure, psia,
L	=	length, ft,
T1	=	temperature of gas at inlet, °R,
S	=	specific gravity of gas,
and
Z	=	compressibility factor for gas, dimensionless.

#### Panhandle equation
This equation is used for moderate-Reynolds-number flows where the Moody friction factor is independent of relative roughness and is a function of Reynolds number to a negative power.
 (Eq. 14)
where
E	=	efficiency factor (new pipe: 1.0; good operating conditions: 0.95; average operating conditions: 0.85),
Qg	=	gas-flow rate, MMscf/D,
d	=	pipe ID, in.,
P1	=	upstream pressure, psia,
P2	=	downstream pressure, psia,
Lm	=	length, miles,
T1	=	temperature of gas at inlet, °R,
S	=	specific gravity of gas,
and
Z	=	compressibility factor for gas, dimensionless.

#### Spitzglass equation

 (Eq. 15)
where
Qg	=	gas-flow rate, MMscf/D,
ΔhW	=	pressure loss, inches of water,
and
d	=	pipe ID, in.

Assumptions:
f	=	(1+ 3.6/ d + 0.03 d ) (1/100),
T	=	520°R,
P1	=	15 psia,
Z	=	1.0,
and
ΔP	=	< 10% of P 1 .

### Application of the formulas
As previously discussed, there are certain conditions under which the various formulas are more applicable. A general guideline for application of the formulas is given next.
#### Simplified gas formula
This formula is recommended for most general-use flow applications.
#### Weymouth equation
The Weymouth equation is recommended for smaller-diameter pipe (generally, 12 in. and less). It is also recommended for shorter lengths of segments ( < 20 miles) within production batteries and for branch gathering lines, medium- to high-pressure (+/–100 psig to > 1,000 psig) applications, and a high Reynolds number.
#### Panhandle equation
This equation is recommended for larger-diameter pipe (12-in. diameter and greater). It is also recommended for long runs of pipe ( > 20 miles) such as cross-country transmission pipelines and for moderate Reynolds numbers.
#### Spitzglass equation
The Spitzglass equation is recommended for low-pressure vent lines < 12 in. in diameter (ΔP < 10% of P1).
The petroleum engineer will find that the general gas equation and the Weymouth equation are very useful. The Weymouth equation is ideal for designing branch laterals and trunk lines in field gas-gathering systems.

## Compression Theory

Both positive displacement and dynamic compressors are governed by a few basic principles derived from the laws of thermodynamics. See the chapter on thermodynamics in the General Engineering volume of this Handbook for a basic discussion of thermodynamics. This section defines terminology and discusses the operating principles essential for understanding compressor design, operation, and maintenance.
### Isentropic (Adiabatic) Compression
An adiabatic process is one in which no heat is added or removed from the system. Adiabatic compression is expressed by
....................(7.1)
where k = Cp/Cv = ratio of specific heats, dimensionless.
Although compressors are designed to remove as much heat as possible, some heat gain is inevitable. Nevertheless, the adiabatic compression cycle is rather closely approached by most positive displacement compressors and is generally the base to which they are referred.
### Polytropic Compression
A polytropic process is one in which changes in gas characteristics during compression are considered. Dynamic compressors generally follow the polytropic cycle as defined by the formula
....................(7.2)
where n = polytropic exponent.
The polytropic exponent n is experimentally determined for a given type of machine and may be lower or higher than the adiabatic exponent k. Because the value of n changes during the compression process, an average value is used.
When inlet and discharge pressures and temperatures are known, the polytropic exponent can be determined from the relationship
....................(7.3)
### Head
Head is simply the work expressed in foot pounds per pound of gas or N-m/kg. At a given compressor speed and capacity, the head developed by a centrifugal compressor is the same regardless of the nature of the gas being compressed. The pressure rise produced by the given amount of head varies with the density of the gas.
Isentropic (Adiabatic) Head. In an isentropic compression process, head is calculated by Eq. 7.4.
....................(7.4)
where
His	=	isentropic head, ft-lbf/lbm,
zavg	=	average compressibility factor, dimensionless,
Ts	=	suction temperature, °R,
S	=	gas specific-gravity (standard atmospheric air = 1.00),
Pd	=	discharge pressure, psia,
and
Ps	=	suction pressure, psia.

Polytropic Head. In a polytropic compression process, head is defined by
....................(7.5)
where
Hp	=	polytropic head, ft-lbf/lbm,
and
ηp	=	polytropic efficiency.

### Adiabatic (Isentropic) Efficiency
Adiabatic efficiency is defined as the ratio of work output for an ideal isentropic compression process to the work input to develop the required head.
For a given compressor operating point, the actual or predicted isentropic efficiency can be calculated with Eq. 7.6.
....................(7.6)
where
ηis	=	isentropic efficiency,
Ts	=	suction temperature, °R,
Td	=	discharge temperature (actual or predicted), °R,
and
k	=	ratio of specific heats, Cp/Cv.

### Polytropic Efficiency
The efficiency of the polytropic compression process is given by
....................(7.7)
where ηp = polytropic efficiency.
### Compressibility Factory
The perfect gas equation derived from Charles’ and Boyle’s laws makes it possible to determine the weight of a given gas as determined by the equation
....................(7.8)
where
P	=	pressure,
V	=	volume,
N	=	number of moles,
R	=	constant for a specific gas,
and
T	=	temperature.

In reality, all gases deviate from the ideal gas laws to some degree. This deviation is defined as a compressibility factor, z , applied as a multiplier to the basic formula. Therefore, Eq. 7.8 is modified to include the compressibility factor as shown next.
....................(7.9)
### Flow (Capacity)
Compressor flow (capacity) can be specified in three ways: mass (weight) flow, standard volume flow, and actual (inlet) volume flow.
Mass (Weight) Flow. Mass flow is expressed as mass per unit of time, most often pounds-mass per minute (lbm/min) or kilograms per minute (kg/min). Mass flow is a specific value independent of gas properties and compressor inlet conditions. Mass flow can be specified on either a wet (water vapor included) or dry basis.
Standard Volume Flow. Standard volume flow is the most common term used by the industry to describe volumetric flow because it is independent of actual gas pressures or temperatures. It is the volume per unit of time using pressures and temperatures that have been corrected to "standard" conditions. These conditions apply to pressure, temperature, molecular weight, and compressibility. The standards must be known and held constant. For purposes of this text, the standard conditions used are
pressure	=	14.7 psia,
temperature	=	60 °F,
compressibility	=	1.00,
and
molecular weight	=	MW of subject gas.

Standard volume flow is usually dry and expressed in millions of standard cubic feet per day (MMScf/D).
Actual (Inlet) Volume Flow. Actual volume flow is defined as the amount of volume per unit of time at the inlet to the compressor. Actual volume flow is normally expressed in actual cubic feet per minute (ACFM) or actual cubic meters per hour (m3/hr). When gas composition and pressure and temperature are known, the specification of actual volume is appropriate because the fundamental performance characteristic of the compressor is sensitive only to actual volume flow at the inlet (see Sec. 7.4.2).
Mass flow can be converted to actual volume flow with Eq. 7.10.
....................(7.10)
where
W	=	mass flow, lbm/min.,
R	=	universal gas constant = 1,545,
MW	=	molecular weight,
Ts	=	suction temperature, °R,
zs	=	compressibility at inlet,
and
Ps	=	absolute suction pressure, psia.

Standard volume flow can be converted to actual volume flow with Eq. 7.11.
....................(7.11)
where Qg = standard volume flow, MMscf/D.
### Compression Ratio
Compression ratio, Rc, is simply the absolute discharge pressure divided by the absolute suction pressure. As expressed in Eq. 7.3, temperature ratio increases with pressure ratio. Temperature limits related to the mechanical design of compressors often will dictate the maximum pressure ratio that can be achieved in a stage of compression. (Refer to Sec. 7.3.9 for a related discussion on intercooling.)
### Intercooling
Where large pressure ratios are needed, splitting the compression duty into one or more stages with intercooling between stages can be the most energy efficient arrangement. The energy savings must be compared with the capital and maintenance investment necessary to provide the cooling. In addition to the thermodynamic benefit, intercooled compression systems result in lower discharge temperatures, which reduce the need for special compressor materials.
### Power Requirement
The total power requirement of a compressor for a given duty is the sum of the gas power and the friction power. The gas power is directly proportional to head and mass flow and inversely proportional to efficiency. Mechanical losses in the bearings and, to a lesser extent, in the seals are the primary source of friction power.
For centrifugal compressors, the gas power can be calculated as
....................(7.12)
where
GHP	=	gas power, horsepower,
W	=	mass flow, lbm/min.,
and
Hp	=	polytropic head, ft-lbf/lbm.

For reciprocating compressors, the gas power can be calculated as
....................(7.13)
where
P1	=	inlet pressure, psia,
V1	=	inlet volume, ACFM,
P2	=	discharge pressure, psia,
and
CE	=	compression efficiency (assume 0.85 for estimating purposes).

### Compressor Selection
Proper selection of the compressor type and number of stages can be accomplished only after considering a number of factors. (For the purposes of this chapter, discussion is limited to centrifugal vs. reciprocating compressors.) Basic information needed for the proper selection includes volume and mass flow of gas to be compressed, suction pressure, discharge pressure, suction temperature, gas specific gravity, and available types of drivers.
The required volume flow and discharge pressure define a point on a graphic representation of compressor coverage, as shown in Fig. 7.6. Examination of this chart reveals that, in general, centrifugal compressors are appropriate for high flow applications, and reciprocating compressors are better suited to low flow rates.
Fig. 7.6—Compressor selection. Areas indicate regions of best performance (courtesy of Dresser-Rand).

### Number of Stages of Compression
Using the specified overall pressure ratio and suction temperature (and an assumed efficiency), the discharge temperature for compression of gas with a known k value in a single stage can be estimated by rewriting Eq. 7.7.
....................(7.14)
where
T2	=	estimated absolute discharge temperature, °R,
T1	=	specified absolute suction temperature, °R,
P1	=	specified absolute suction pressure, psia,
P2	=	specified absolute discharge pressure, psia,
k	=	ratio of specific heats,
ηp	=	assumed polytropic efficiency,
	≈	0.72 to 0.85 for centrifugal compressors,
and
	≈	1.00 for reciprocating compressors.

If the single-stage discharge temperature is too high (typical limit is 300 to 350 °F), it is necessary to configure the compression equipment in more than one stage. Calculating the compression ratio per stage with Eq. 7.15 does the evaluation of a multistage design.
....................(7.15)
where
Rsect	=	compression ratio per section,
and
n	=	number of sections.

Using the previous equations and prudent assumptions, it is possible to determine the minimum number of stages required to accomplish a given overall compression ratio without exceeding temperature limits.